## Slide 1
ANNEX VI - INDIVIDUAL LATRINE OPTIONS IN RAKHINE STATE
INDIVIDUAL LATRINE WITH BAMBOO EARTHEN LID 4‘ x 4‘ x 7‘ – 6”
Myanmar WASH Cluster http://www.themimu.info/emergencies/wash-cluster
Estimated materials package cost per household latrine : USD 80 (concrete footings not included in this price)
Family shares all other associated or extra cost related to construction
Technical Specifications:
Bamboo lined pit latrine with bamboo and soil cover
Myaw Posts : 4"dia x 12'
Woven bamboo mat for walling and Bamboo rings for pit
Floor : 6"x1"x12‘ Hardwood
Beams : 3"x2"x12' Hardwood
Beams :2"x1"x12' Hardwood
CGI sheets
Tarpaulin sheet to cover pit
Plastic Pan & 3" PVC Pipe
Ventilation pipe and PVC bracket
Door Handle & 4” hinge
Bolt 4"
Nylon rope & Binding wire
Assorted nails of various sizes

## Slide 2
ANNEX VII - INDIVIDUAL LATRINE OPTIONS IN RAKHINE STATE
INDIVIDUAL LATRINE WITH CONCRETE HAT 4‘ x 4‘ x 7‘ – 6”
Myanmar WASH Cluster http://www.themimu.info/emergencies/wash-cluster
Estimated materials package cost per household latrine : USD 160 (concrete footings not included in this price)
Family shares all other associated or extra cost related to construction
Technical Specifications:
Bamboo lined pit latrine with concrete hat
Myaw Posts : 4"dia x 12'
Woven bamboo mat for walling
Floor : 6"x1"x12‘ Hardwood
Beams : 3"x2"x12' Hardwood
Beams :2"x1"x12' Hardwood
CGI sheets
Concrete ring and lid
Plastic Pan & 3" PVC Pipe
Ventilation pipe and PVC bracket
Door Handle & 4” hinge
Bolt 4“
Nylon rope & Binding wire
Assorted nails of various sizes